## Slide 1
Energy harvesting with wearable jackets is useful. Examples are:
  powering up mobile devices in remote or disaster areas, and
  soldiers who carry power hungry electronic gears in battle fields, where line power is often unavailable.
Outdoor solar energy and body heat are good candidates.
Motivation
Solar and Thermal Energy Harvesting with a Wearable Jacket
Quinn Brogan, Thomas O’Connor, and Dong Sam Ha
Dept. of Electrical and Computer Eng.
Virginia Tech, Blacksburg, Virginia USA
The average power harvested:
  Sunny Day: 475 mW to 500 mW.
  Partly cloudy day: 340 mW
  Very cloudy day and in full shade: 140 - 220 mW
The power generated by TEGs lies in µW range due to the low temperature gradient available within the jacket.
Transducers & Batteries
Summary
Proposed System
PV Experimental Results
Four zones of four solar cells are placed on the chest, back, right and left shoulders.
  Accounts for rapid irradiation changes while walking.
A 6x2 array of TEGS are on the chest and back.
  Body heat is the highest, while maintaining comfort of the wearer.
TI BQ25505 chips regulate the output voltage and perform maximum power pont tracking (MPPT) and the battery protection.
Power of Solar Jacket by Section , Stationary
(outside, back facing sun at 4 p.m.)
Power of Solar Jacket by Walking Direction
(full sun days at 1 p.m.)
Power by Section on a Cloudy Day
(walking west at 1 p.m.)
Chart: Time (s)
Chart: Time (s)
TEG Experimental Result
Chart: Time (s)
Chart: Time (s)
Total Power
Back, sun
L. Shoulder, sun
R. Shoulder, shade
Chest, shade
PV Cells:
  Vopen = 2.2 V, Vshort = 50 mA
  Size: 31 mm × 31 mm × 3.0 mm
Thermoelectric Generators: TEC1-12709
  Vmax = 15.4 V, Ishort = 9 A
  Size: 40 mm × 40 mm × 3.6 mm
Two AAA NiMH batteries in series
Full sun
Shade
A thinner out layer with good thermal conductivity could increase the temperature gradient and the power.
Effect of Partial Shading
The prototype system was placed under full sun with a various number of PV cells in total shade.
As the number of shaded cells increases, the amount of harvested power reduces gradually. The gradual degradation of the power is due to the MPPT employed by the TI chips. It is a good contrast with a conventional PV cell configuration, in which a few shaded cells can drastically reduce the total power harvested