## Slide 1: Transimpedance Amplifiers in CMOS Technology
for Optical Communications
over the Data Rate of 40 Gb/s
Joseph Chong
Dept. of Electrical and Computer Eng.
Virginia Tech
April 18, 2014

## Slide 2: Outline
Motivation
Role of Transimpedance Amplifier (TIA)
TIA Circuit Topologies
Recent Literature
Proposed Design
Conclusion

## Slide 3: Motivation
IEEE 802.3 supports 40 Gb/s and 100 Gb/s.
  Achieved with multiple channels such as 4 x 10 Gb/s.
Multiple channels pose drawbacks including:
  Inter-channel crosstalk.
  Large size.
  Possible of larger power consumption
Mitigate drawbacks by reducing the number of channels.
Much more with CMOS technology: lower power comparing to other techs, and enables integration.
Toward future standard of 400 Gb/s, is it possible to get 1 x 100 Gb/s in CMOS?

## Slide 4: Part 1: Role of TIA

## Slide 5: TIA in Optical Receiver
On-off keying modulated input.
Optical  electrical by photodiode.
Iin  Vout with TIA.
Restores clock & process data.

## Slide 6: Photodiode
A P-I-N diode has a wider depletion region.
Reversed biased and equivalent to a capacitor.
Optical power input controls an AC current source.

## Slide 7: TIA Performance
TIA dominates performance of receiver.
Performance metrics:
  Gain
  Group delay variation
  Bandwidth
  Noise
Will be discussed in next section.

## Slide 8: Transimpedance Gain
Transfer function:
In decibel (dB) scale:
Transimpedance gain

## Slide 9: Group Delay
Transfer function
Obtain group delay (GD) from phase.
Group delay variation (GDV) is τmax – τmin within bandwidth.

## Slide 10: Bandwidth
A digital signal has wide range of frequency components.
Bandwidth (BW) of TIA requires a pass band from near DC to near f0.
3-dB frequency is where ZT is 1/2 of low frequency gain.
A rule of thumb relates 3-dB freq. to data rate.
f0
f3dB
Image courtesy of http://edn.com/design/test-and-measurement/4422710/The-basics-of-digital-signal-spectra

## Slide 11: Bandwidth
Image courtesy of http://edn.com/design/test-and-measurement/4422710/The-basics-of-digital-signal-spectra
40 Gb/s
f0 = 40 GHz
f3dB = 28 GHz
100 Gb/s
f0 = 100 GHz
f3dB = 70 GHz
f0
f3dB

## Slide 12: Part 2: Representative TIA

## Slide 13: Representative TIA
Two commonly used circuit topologies:
  Common gate (CG) amplifier
  Shunt-feedback (S-FB) amplifier

## Slide 14: CG: Gain and Bandwidth
Transfer function:
Pole frequency associated with CPD:
Increase gm1 for larger bandwidth.
  Increase width of M1  larger Cgs
  Increase bias current  RD voltage drop
0
Low freq gain = RD
0

## Slide 15: CG: Noise at Vout
Noise from RD:
Noise from M1 and M2 :
Vout due to superposition of current sources :
How to compare noise with other TIA?
Larger gain  larger output noise, but not worse signal-to-noise ratio.

## Slide 16: Input Referred Noise
Compare by the equivalent input noise current (input referred noise).
Calculation procedure:
  Output noise due to resistor RD
  Transfer function
  Input referred noise
Enables fair comparisons between designs.

## Slide 17: CG: Input Referred Noise
Express noise in current density: mean square current per hertz.
Observe from equation above, noise of RD and M2 is directly referred to the input.

## Slide 18: S-FB: Gain and Bandwidth
A Shunt feedback (S-FB) amplifier is composed of a voltage amplifier with gain –A and RF as feedback.
Transimpedance gain
Pole frequency
0
1
At A>>1, Low freq gain = RF

## Slide 19: S-FB: Input Referred Noise
Noise of amplifier A is modeled as voltage
Input referred noise:

## Slide 20: Comparison: Noise
Comparing low frequency noise
  The noises from RD and RF are identical.
  The noise from Vn,A can be smaller than the noise from M2.

## Slide 21: Comparison: Bandwidth
CG’s dominant pole is associated with 1/gm.
S-FB’s pole is associated with RF/A, which can be larger than 1/gm.

## Slide 22: Possibility for 40 Gb/s?
Some numerical examples for the two topologies.
ZT = RD = RF = 200 = 46dB
Input pole frequency = 15.9GHz.
How to achieve 40Gb/s?

## Slide 23: Filling the Gap

## Slide 24: Part 3: Recent Literature (Bandwidth Enhancement Techniques)

## Slide 25: Methods of Bandwidth Enhancement
Series interstage inductor
π-type inductor network
Triple resonance network
gm-boosting topology
Inductors
Circuit Topology

## Slide 26: Series Inductor (1)
Transfer function:
Parameters:
J. Kim and J. F. Buckwalter, “Bandwidth Enhancement With Low Group-Delay Variation for a 40-Gb/s Transimpedance Amplifier,” IEEE Trans. Circuits Syst. I Regul. Pap., vol. 57, no. 8, pp. 1964–1972, 2010.

## Slide 27: Series Inductor (2)
Group Delay
Gain
GDV
BW
Optimal m value, which translates to L value, provides adequate BW enhancement and minimal GDV.
J. Kim and J. F. Buckwalter, “Bandwidth Enhancement With Low Group-Delay Variation for a 40-Gb/s Transimpedance Amplifier,” IEEE Trans. Circuits Syst. I Regul. Pap., vol. 57, no. 8, pp. 1964–1972, 2010.

## Slide 28: Series Inductor (3)
The first work (2010) is a S-FB amplifier followed by 2 stages of post-amplifiers in 0.13 µm CMOS.
Bandwidth is extended from 5GHz to 30GHz.
GDV is kept within 12ps.
J. Kim and J. F. Buckwalter, “Bandwidth Enhancement With Low Group-Delay Variation for a 40-Gb/s Transimpedance Amplifier,” IEEE Trans. Circuits Syst. I Regul. Pap., vol. 57, no. 8, pp. 1964–1972, 2010.

## Slide 29: Series Inductor (4)
The second work (2012) is a push-pull S-FB amplifier followed by one stage of post-amplifier fabricated in 45 nm SOI CMOS.
Bandwidth is extended from 25 GHz to 33 GHz.
GDV is kept within 6ps.
J. Kim and J. F. Buckwalter, “A 40-Gb/s Optical Transceiver Front-End in 45 nm SOI CMOS,” IEEE J. Solid State Circuits, vol. 47, no. 3, pp. 615–626, 2012.

## Slide 30: π-type Inductor Peaking (1)
A π-type inductor peaking utilizes three interstage inductors for bandwidth enhancement purposes.
The small signal equivalent circuit shows that:
  Cd is the drain capacitance of 1st stage.
  Cg is the gate capacitance (of next stage).
J.-D. Jin and S. S. H. Hsu, “A 40-Gb/s Transimpedance Amplifier in 0.18-um CMOS Technology,” IEEE J. Solid State Circuits, vol. 43, no. 6, pp. 1449–1457, 2008.

## Slide 31: π-type Inductor Peaking (2)
Gain enhancement of more than 3 times is achieved.
J.-D. Jin and S. S. H. Hsu, “A 40-Gb/s Transimpedance Amplifier in 0.18-um CMOS Technology,” IEEE J. Solid State Circuits, vol. 43, no. 6, pp. 1449–1457, 2008.

## Slide 32: π-type Inductor Peaking (3)
Jin and Hsu proposed a four-stage common source amplifier with π-type inductor peaking in 0.18 µm CMOS.
3-dB bandwidth is extended from 5GHz to 30GHz.
J.-D. Jin and S. S. H. Hsu, “A 40-Gb/s Transimpedance Amplifier in 0.18-um CMOS Technology,” IEEE J. Solid State Circuits, vol. 43, no. 6, pp. 1449–1457, 2008.

## Slide 33: TRN (1)
A triple resonance network (TRN) is composed of one series inductor and one shunt inductor.
Reverse TRN has R1 and L1 connected to C2.
Entire network can be simplified as a circuit of C parallel with RL.
C.-F. Liao and S.-I. Liu, “40 Gb/s Transimpedance-AGC Amplifier and CDR Circuit for Broadband Data Receivers in 90 nm CMOS,” IEEE J. Solid-State Circuits, vol. 43, no. 3, pp. 642–655, 2008.

## Slide 34: TRN (2)
Drain impedance:
Three resonance frequencies:
  ω1: ( Req and Leq branch is inf.)
  ω2: ( Ceq branch is inf.)
  ω3: Ztot is pure resistive
C.-F. Liao and S.-I. Liu, “40 Gb/s Transimpedance-AGC Amplifier and CDR Circuit for Broadband Data Receivers in 90 nm CMOS,” IEEE J. Solid-State Circuits, vol. 43, no. 3, pp. 642–655, 2008.

## Slide 35: TRN (3)
A S-FB CG in 90 nm CMOS by Liao and Liu (2008).
Bandwidth enhancement from 5GHz to 40GHz.
C.-F. Liao and S.-I. Liu, “40 Gb/s Transimpedance-AGC Amplifier and CDR Circuit for Broadband Data Receivers in 90 nm CMOS,” IEEE J. Solid-State Circuits, vol. 43, no. 3, pp. 642–655, 2008.

## Slide 36: Inductor Peaking Downsides
Three types of inductor peaking presented shows attractive results
However, there are some downsides.
  Inductors occupies large chip area.
  Large inductors have low self resonance freq.
  On chip inductors have low Q value.
  Series inductors extend bandwidth while increasing frequency dependent delay.

## Slide 37: Implementation of On Chip Inductors
On chip inductors are implemented as spiral metal.
Commonly used model shows capacitance coupling, parasitic loss and substrate loss.

## Slide 38: Inductor Parameters
Convert the inductor model to a parallel RLC circuit.
Definition of self resonance frequency (SRF):
Definition of Q value:

## Slide 39: Self Resonance Frequency
After the inductor’s self resonance frequency, capacitance becomes dominant in the structure.
imag(Z)/ω
freq (GHz)
inductor
capacitor

## Slide 40: Effect of Q value
Lower Q value causes deterioration of bandwidth enhancement effect.
Q=25
Q=10
No Inductor
Normalized Vout (dB)
freq (GHz)

## Slide 41: gm-boosting (1)
Based on CG amplifier M1 and R1.
Common source M2 and R2 feeds to gate of M1.
Input resistance:
Transfer function:
Pole associated with CPD:

## Slide 42: gm-boosting (2)
Bashiri and Plett (2010) proposed gm-boosting with inductor peaking design in 65nm CMOS.
Achieves 2 times bandwidth enhancement.
S. Bashiri and C. Plett, “A 40 Gb/s transimpedance amplifier in 65 nm CMOS,” in IEEE International Symposium on Circuits and Systems (ISCAS), 2010, pp. 757–760.

## Slide 43: Summary of Techniques
Ref. | CMOS Process | ZT (dBΩ) | Enhanced BW | Bandwidth Enhancement Techniques
Jin & Hsu 2008 | 0.18 μm | 51 | 30.5 | π-type inductor peaking
Liao & Liu 2008 | 90 nm | 60 | 40 | Reverse triple resonance
Kim & Buckwalter 2010 | 0.13 μm | 50 | 29 | Series interstage inductor
Kim & Buckwalter 2012 | 45 nm SOI | 55 | 41 | Series interstage inductor
Bashiri & Plett 2010 | 65 nm | 46.7 | 38 | gm-boosting with inductors
>28GHz, Works at 40 Gb/s!

## Slide 44: Part 4 Proposed Design for 100 Gb/s

## Slide 45: Overall Circuit
gm-boosting transimpedance stage
Capacitive degeneration stage
Inductive peaking
Differential signaling

## Slide 46: gm-boosting Stage
Transfer function:
L1 and L3 introduce peaking in transfer function.

## Slide 47: Capacitive Degeneration
Voltage gain function:
Zero can be used to compensate a pole.

## Slide 48: TIA Bandwidth and Gain
Bandwidth: 75 GHz >70GHz, Works at 100 Gb/s!
Gain: 40 dBΩ
75
-3dB

## Slide 49: Comparison
Figure of merit “BW(GHz) x ZT,mag / Power (mW)”.
Ref. | Process | BW (GHz) | ZT (dBΩ) | GDV (ps) | Noise (pA/√Hz) | Power (mW) | FOM
Proposed Design | 65 nm | 75 | 40 | 8.7 | 31 | 24 | 312.5
Jin & Hsu 2008 | 0.18 μm | 30.5 | 51 | 150 | 55.7 | 60.1 | 180.1
Liao & Liu 2008 | 90 nm | 22 | 60 | n/a | 22 | 75 | 293.3
Kim & Buckwalter 2010 | 0.13 μm | 29 | 50 | 12 | 51.8 | 45.7 | 200.7
Kim & Buckwalter 2012 | 45 nm SOI | 30 | 55 | 7.8 | 20.5 | 9 | 1874.5
Bashiri & Plett 2010 | 65 nm | 19 | 46.7 | 13 | 30 | 39.9 | 103.0

## Slide 50: Conclusion
IEEE standard has motivated several 40 Gb/s TIA in CMOS, which target low power and high integration application.
Most TIA designs are based on CG or S-FB circuit.
Bandwidth enhancement techniques are necessary for 40 Gb/s and beyond.
Inductor peaking is the most widely used technique.
A TIA designed in 65nm CMOS achieves 75 GHz bandwidth, shows promising results to work at a 100 Gb/s data rate.

## Slide 51: Reference
B. Razavi, Design of Integrated Circuits for Optical Communications, 2nd ed., Wiley, 2012.
B. Razavi, RF Microelectronics, 2nd ed., Pearson Education, 2012.
J. Kim and J. F. Buckwalter, “Bandwidth Enhancement With Low Group-Delay Variation for a 40-Gb/s Transimpedance Amplifier,” IEEE Trans. Circuits Syst. I Regul. Pap., vol. 57, no. 8, pp. 1964–1972, 2010.
J. Kim and J. F. Buckwalter, “A 40-Gb/s Optical Transceiver Front-End in 45 nm SOI CMOS,” IEEE J. Solid State Circuits, vol. 47, no. 3, pp. 615–626, 2012.
J.-D. Jin and S. S. H. Hsu, “A 40-Gb/s Transimpedance Amplifier in 0.18-um CMOS Technology,” IEEE J. Solid State Circuits, vol. 43, no. 6, pp. 1449–1457, 2008.
C.-F. Liao and S.-I. Liu, “40 Gb/s Transimpedance-AGC Amplifier and CDR Circuit for Broadband Data Receivers in 90 nm CMOS,” IEEE J. Solid-State Circuits, vol. 43, no. 3, pp. 642–655, 2008.
S. Bashiri and C. Plett, “A 40 Gb/s transimpedance amplifier in 65 nm CMOS,” in IEEE International Symposium on Circuits and Systems (ISCAS), 2010, pp. 757–760.

## Slide 52: Thank you!